Teensy Audio Platform
Looking at the Teensy Audio platform with an
eye towards sound synthesis
Presented By:
Marshall Taylor
Byron Jacquot
SparkFun Electronics
Niwot, Colorado

---
Part I: Background
What Is Teensy?
Small, inexpensive, Arduino-compatible microcontroller boards.
[photos]
From PJRC.com
Three Generations:
- 1.0 Atmel AVR Mega328P
- 2.0 Atmel ATMEGA32U4 – native USB port.
- 3.1/3.2 Freescale Kinetis MK20DX256 (ARM Cortex M4)
- LC (Low Cost) Cortex M0+
Programming environment is FOSS – GCC for ARM, Arduino IDE.

---
Teensy 3.2
[pic]
Microcontroller Features:
- 32-bit ARM core
- 256 kB flash memory
- 64 kB RAM
- 34 I/O pins
- 21 Analog-to-digital channels
- DMA (direct memory access)
- I2S Peripheral
- Integer DSP instructions

---
Teensy Audio Adapter
[pic]
[block diagram from datasheet]
Shield board with stereo audio codec and micro-SD card slot.
Codec - “coder/decoder” combines audio-type analog-to-digial and digital-to-analog converters.
The codec on the shield is capable of 2 channels 16-bit audio conversion.
It also provides some audio utility functions – input and output gain control, EQ, bass enhancement, limiting, and a headphone amplifier.

---
Part 2: Using Teensy Audio
Browser based block interface built on Node Red framework. Can run locally w/o internet connection.
Drag and drop DSP functions, wire them together with virtual patch cords.
It also functions as the reference manual for the DSP nodes.
-demo part 1-
Show off types of nodes

---
Arduino Details
Supports Teensy when the “Teensyduino” package is loaded, and Teensy is selected as the target.
It's not a terribly rich environment.
- The code editor is minimal but functional.
- It's not a debugger. But there is a serial window.
- The build process is really coarse –
  - The first build after it's launched will build all dependencies. Subsequent builds don't rebuild everything.
  - Dependencies are determined through a set of paths.

---
To Load A Patch
Hit the “export” button in GUI, and copy the code listing to the clipboard.
Paste that code into the local declarations of an Arduino Sketch.
Typically, you'll need to add some initialization code to the setup() function.
-demo part 2-

---
How Others are Using Teensy Audio
Two types of project seem to be most common:
1. Sample playback from SD cards.
2. Realtime analysis – can do 1024 point FFT.

---
Part 3: How We're using Teensy Audio
Synthesis and effects!
Teensy has many channels of onboard utilitarian (non-Audio) ADC, so we can add knobs for realtime control.
Also has serial ports for MIDI.
I2C and SPI for low-level hardware interfaces.

---
Quick Commercial Break
Protos shown tonight were made with CNC tools.
Acrylic was worked withan Epilog laser cutter.
Wooden end caps were made using Shapeoko CNC router.
...

---
Bendvelope
...

---
Effects
Modulated delay block.
The core of a tape-delay emulation and chorus.
...
Demo?

---
Teensy-boom
Classic-style drum machine with step sequencer.
Drums are based on analog emulation.
- Drum voices are presently using direct-digital-synthesis (DDS) waveform generation for damped sine waves.
- Cymbal voices use an emulation of the TR-808/606 cymbal circuit, generating and combining square waves
- ...

---
The more we learn about the platform, the more ideas we dream up...

---
Part 4: Lifting The Hood
Architecture
[pic]
Codec-i2s-dma
128 sample blocks arrive without any software intervention.
Expected to deliver 128 sample blocks to the output, fed out by hardware
Dma-i2s-codec

---
Software Architecture
A lot of pieces are generic, and hidden behind the scenes.
- DMA and I2S drivers
- Graph analysis of the patch represented by the nodes and connectors. The connectors correspond to the runtime RAM usage, but it appears to be reasonably optimal. The memory for the connectors has to be allocated by the sketch using ___.
- Execution model can be considered as two threads.
  - The Arduino sketch is a lower priority thread that can control the processing.
  - The processing is done by the nodes in an interrupt (IE. higher priority thread).
- The processing work is done by the nodes.
  - Each note is a C++ class, derived from a common __ ancestor.
  - Each uses the parent class for sample buffer management
  - Each must implement the update() function.
  - Other functions are more dependent on the use & behavior of the block.

---
The update() Function
Writing a new node is mainly about writing it's update() function. Update does the realtime processing of blocks of PCM data.
- Called automatically by framework when audio sample data is required.
- Can generate, consume or pass through.
- Nodes can have [0..many] inputs, and [0..many] outputs.
- Needs to be somewhat lightweight, and shouldn't use blocking resources.
If the node needs to receive data from the sketch, that's usually done by adding accessor functions.

---
Comparison to VST Plugin Architecture
- Both are frameworks for handling DSP routines.
- VST uses variable sized sample blocks. So far Teensy uses fixed size blocks.
- VST uses floats on range [0..1.0] for control parameters. Teensy has no limitation.
- VST uses floats in range [-1.0..1.0] for audio data. Teensy uses 16-bit signed integers.

---
Fixed Point Math
The thing that makes this possible is fast multiplication hardware in the CPU. It can handle integer multiplication quickly, for 16 and 32 bit data. Floating point is considerably slower.
Rather than thinking about the PCM data as being 2's complement signed integers [-32768..32767], it's easier to reframe it as being fractional data from [-1..0.999999]
A byte then breaks down as follows
[pic – byte breakdown, fractional bits, signed vs unsigned]
Longer integer types can use the same format, with progressively smaller fractional bits.
[pic...]
Conversion between lengths means left-justifying the data, and adding or discarding LSBs.

---
Fixed Point Math, Page 2
The trick to using fixed point math is a reexamination of the multiplicative identity. We know that multiplying x by 1 results in x.
If we multiply two fixed point numbers, we get similar behavior
0xff x 0xff = 0xfe01
If we discard the eight fractional bits that were added (just as we might limit the number of digits of precision in a decimal calculation), we nearly return to the multiplicative identity.
0xFe01 >>= 8 -> 0xfe.
(Nearly because 0xff isn't a complete 1, it's 255/256, or 0.99605...)
This also works for twos-complement numbers, but every multiplication adds two sign bits, so we need to shift by fewer bits to discard LSBs.
0x7f * 0x7f = 0x3f01
3f01 >>= 7 -> 0x7e

---
Using the fast multiplies
[quote Knuth on Opt.]
Most legible: Can simply use C-style math operators, and the compiler generates reasonable code, inserting those instrs when possible.
More optimized: Dspinst.h contains explicit wrappers around useful DSP instructions
q31*q31>>32!
Arm_math.h has a lot of useful, type-specific, functions, but they're not as fast as the DSP instructions.

---
Useful Development Tricks
- Clone & Mutate existing classes.
- Or at least use the existing classes for reference.
- You can print diagnostic information from update() function, but it's easy to overwhelm the system if you do it for every sample or block. Set a flag periodically, or add a sketch-task inspect() method.
- Periodically measure system load for CPU % and buffer consumption.
- Turn off audio interrupts if you need to guarantee atomiticity of class accessors (ie trigger env and reset osc phase).
- Allocate buffer mem and be sure to enable and turn on the output volume control!

---
Resources
- PJRC.com
- http://www.pjrc.com/teensy/gui/
- Github.com/paul....audio...
- https://github.com/Jacquot-SFE/Teensy-synth-platform - this presentation is in there.